PC1 : 10.10.1.98 & 255.255.255.224	10.10.1.97
FE80::260:47FF:FECA:4DEE

PC2 : 2001:DB8:1:1::2/64	FE80::1
FE80::2E0:B0FF:FE35:82B8

PC3 : 10.10.1.18 & 255.255.255.240	10.10.1.17
FE80::260:70FF:FE34:6930

PC4 : 2001:DB8:1:4::2/64	FE80::2
FE80::206:2AFF:FEBC:7CD4

Test ping PC1 vers PC3 :
C:\>ping 10.10.1.18
Pinging 10.10.1.18 with 32 bytes of data:
Reply from 10.10.1.97: Destination host unreachable.
Reply from 10.10.1.97: Destination host unreachable.
Reply from 10.10.1.97: Destination host unreachable.
Reply from 10.10.1.97: Destination host unreachable.
Ping statistics for 10.10.1.18:
Packets: Sent = 4, Received = 0, Lost = 4 (100% loss),

trace PC1 vers PC3 :
C:\>tracert 10.10.1.18
Tracing route to 10.10.1.18 over a maximum of 30 hops:
1 1 ms 0 ms 0 ms 10.10.1.97

trace PC3 vers PC1 :
C:\>tracert 10.10.1.98
Tracing route to 10.10.1.98 over a maximum of 30 hops:
1 1 ms 0 ms 0 ms 10.10.1.17

R1 :
R1>en
R1#show ip interface brief
Interface IP-Address OK? Method Status Protocol
GigabitEthernet0/0 unassigned YES unset up up
GigabitEthernet0/1 10.10.1.97 YES manual up up
Serial0/0/0 unassigned YES unset administratively down down
Serial0/0/1 10.10.1.6 YES manual up up
Vlan1 unassigned YES unset administratively down down

R2 :
R2>en
R2#conf t
Enter configuration commands, one per line. End with CNTL/Z.
R2(config)#interface serial 0/0/0
R2(config-if)#ip address 10.10.1.5 255.255.255.252
R2(config-if)#no shut
R2#show ip interface brief
Interface IP-Address OK? Method Status Protocol
GigabitEthernet0/0 unassigned YES unset administratively down down
GigabitEthernet0/1 unassigned YES unset administratively down down
Serial0/0/0 10.10.1.5 YES manual up up
Serial0/0/1 10.10.1.9 YES manual up up
Vlan1 unassigned YES unset administratively down down
R2#show ip route
Codes: L - local, C - connected, S - static, R - RIP, M - mobile, B - BGP
D - EIGRP, EX - EIGRP external, O - OSPF, IA - OSPF inter area
N1 - OSPF NSSA external type 1, N2 - OSPF NSSA external type 2
E1 - OSPF external type 1, E2 - OSPF external type 2, E - EGP
i - IS-IS, L1 - IS-IS level-1, L2 - IS-IS level-2, ia - IS-IS inter area
* - candidate default, U - per-user static route, o - ODR
P - periodic downloaded static route
Gateway of last resort is not set
10.0.0.0/8 is variably subnetted, 6 subnets, 4 masks
C 10.10.1.4/30 is directly connected, Serial0/0/0
L 10.10.1.5/32 is directly connected, Serial0/0/0
C 10.10.1.8/30 is directly connected, Serial0/0/1
L 10.10.1.9/32 is directly connected, Serial0/0/1
D 10.10.1.16/28 [90/2170112] via 10.10.1.10, 00:13:05, Serial0/0/1
D 10.10.1.96/27 [90/2170112] via 10.10.1.6, 00:00:29, Serial0/0/0

Test ping PC1 vers PC3 (2) :
C:\>ping 10.10.1.18
Pinging 10.10.1.18 with 32 bytes of data:
Reply from 10.10.1.18: bytes=32 time=3ms TTL=125
Reply from 10.10.1.18: bytes=32 time=11ms TTL=125
Reply from 10.10.1.18: bytes=32 time=3ms TTL=125
Reply from 10.10.1.18: bytes=32 time=10ms TTL=125
Ping statistics for 10.10.1.18:
Packets: Sent = 4, Received = 4, Lost = 0 (0% loss),
Approximate round trip times in milli-seconds:
Minimum = 3ms, Maximum = 11ms, Average = 6ms

Test trace PC1 vers PC3 :
tracert 10.10.1.18
Tracing route to 10.10.1.18 over a maximum of 30 hops:
1 1 ms 0 ms 0 ms 10.10.1.97
2 1 ms 2 ms 1 ms 10.10.1.5
3 1 ms 2 ms 1 ms 10.10.1.10
4 0 ms 1 ms 10 ms 10.10.1.18
Trace complete.